1)

[[1,0,0,3.73],[0,1,0,0],[0,0,1,2.73],[0,0,0,1]]

2)

[[0,0,0,0,0,0],[0,1,1,1,0,0],[1,0,0,0,0,1],[0,0,1,-0.73,0,0],[-1,0,0,0,0,-3.73],[0,1,2.73,3.73,1,0]]

3)

[[0,0,0,0,0,0],[0,1,1,1,0,0],[1,0,0,0,0,1],[0,2.73,3.73,2,0,0],[2.73,0,0,0,0,0],[0,-2.73,-1,0,1,0]]

4)

[[0.5,0.87,0,1],[0.22,-0.13,-0.97,-1.9],[-0.84,0.48,-0.26,-4.5],[0,0,0,1]]

5)

same as 4

algorithm for FK (in space coordinates)

available:
- R6 vector S consisting of R3 vector w (angular velocity) and R3 vector v (linear velocity) for each joint. S can be identified visually from the robot model

- end-effector transformation matrix M (in the robot's 'zero' or 'home' position) which can be identified visually from the robot model

- list of theta angles (theta 1 through theta n) for the n axes

needed:
- transformation matrix T of the end-effector frame given a particular set of joint coordinates **theta**, i.e. the position and orientation of the end-effector frame given a certain pose of the robot.

algorithm steps:
1. calculate S in se3 (skew-symmetric) matrix **S_se3** for each S

2. find transformation matrix **T(n)** for each joint by calculating the matrix exponential of each **S_se3** multiplied with the respective angle **theta(n)**. The matrix exponential is calculated in Scipy or Matlab/Octave as **expm(V_adj*theta(n)**

3. multiply all T(n) together and append M at the end of the product to find **T_FK**